## Slide 1: Sustainable Development at the University of Cambridge. Stewart Bethell University of Cambridge Greg Callaghan Stantec

## Slide 2
Facilitate convenient and predictable travel to the University sites and between University sites for all staff, students and visitors.
Minimise the University’s environmental footprint from transport and improve air quality in Cambridge.
Make a positive contribution to the wellbeing of staff and students and the quality of place, protecting and enhancing Cambridge’s historic and attractive environment.
Contribute to the development of the University estate and working practices in the University to reduce transport demand and reliance on motorised modes.
Exploit emerging and future technologies effectively and make best use of world class research within the University.

## Slide 3
Target: 75% of staff members should regularly commute to work by sustainable modes of travel (walking, cycling, bus, train, motorcycle, car sharing or working at home (i.e. not in a single occupancy car).
It is monitored via an annual staff travel survey.

## Slide 4
University of Cambridge
Buildings

## Slide 5: Applying a vision: 20-minute community Eddington, Cambridge

## Slide 6
A new urban quarter for Cambridge, promoted, developed, and operated by UoC
Edge of City near the M11 and A14 and with relatively poor sustainable travel options at the outset
The development has created trips originating from dwellings to various University operational sites including central Cambridge and Cambridge Biomedical Campus Including social infrastructure including the school, Sainsbury’s, Hotel, and Storey’s Field community centre.

## Slide 7: Proposed Development types
Land Use | Travel patterns differ to the typical as:
Market Housing | Whilst freely available on the open market, people generally do not live within Cambridge to work elsewhere – they’ve “brought in” to the local life style with reduced car usage
Market Flats | 
Key Worker Housing | Restricted / awarded to University Key Workers who work within the University’s facilities throughout Cambridge. Car parking de-coupled from housing, available only upon application, controlled by permit
Key Worker Flats | 
Collegiate Accommodation | Accommodation for post-grads only, subject to the University’s Motor Proctor control
Commercial Research | UofC-related commercial research facilities having far lower car trip generation rates than equivalent commercial science park facilities
Academic Research | Academic research land uses within the Development having limited parking and a lower car-based trip generation than commercial research land uses
Various Ancillary Land Uses | Provided on site to reduce the need to travel for the basics of life

## Slide 8
The TRICS database is the best available and can provide trip generation estimate ranges for a variety of development scenarios.
However, because of the unique nature of the North-West Cambridge Development/Cambridge City setting, which is considered less conventional, a more bespoke approach has been required.
We agreed with CCC to use a “blended” approach to assessing person trips, generally using:
the TRICS database – to assess person trips for each land use; and
bespoke mode share data for each land use – to assign these total person trips by land use, to person trips by modes. National and local data sources used, with some commissioned surveys
Planning Data Requirements

## Slide 9
Land Use | Trip Generation | Mode share
Market Housing | TRICS – All Sites | TRICS - Chesterton Cambridge survey
Market Flats | UofC - Cromwell Road survey (March 2005) | UofC - Cromwell Road survey (March 2005)
Key Worker Housing | UofC - Cromwell Road survey (March 2005) | TRICS / UofC Travel for Work survey (2009 TfW Survey Data for University of Cambridge)
Key Worker Flats | TRICS – All Sites | UofC Travel for Work survey (2009 TfW Survey Data for University of Cambridge)
Collegiate Accommodation | TRICS | Vehicle mode share – TRICS Non-car mode share – UofC Travel for Work survey(2009 TfW Survey Data for University of Cambridge)
Commercial Research | TRICS | Cambridge Science Park Travel for Work survey (2009 TfW Survey Data for Cambridge Science Park)
Academic Research | UofC - CAPE Building survey (April 2010) | UofC CAPE Building survey (April 2010)
School | TRICS | Off-peak hours – TRICS Peak hour - CCC’s Sustainable School Travel Strategy Annual Monitoring Report (11 May 2009)
Stantec Original Data Sources - 2010

## Slide 10
Chart: 
| Multi Vehicle Occupants | Single Vehicle Occupants | Public Transport | Cyclist | Pedestrains
Audience | 0.24 | 0.27 | 0.06 | 0.28 | 0.15
The Transport Assessment reported the following Total 12-hour Base Case Person Trip generation mode shares:
Stantec – Transport Assessment – 2010

## Slide 11
Cambridgeshire County Council Planning requirements:
Annual monitoring of through traffic
Car parking on neighbouring roads to the development
Trip Banking for A14 junction 31, not to exceed 200 trips above baseline
Deliver/Monitor sub-site travel plans
In addition to maintaining the UoC Transport Strategy Modal KPI of 75% or more of trips by sustainable mode.
Transport Monitoring at Eddington

## Slide 12
University’s Transport Team (Manager + Coordinator)
Primary School Travel Coordinator & Parent Travel Committee
Sainsbury’s
Travel Coordinator
Community Centre Travel Coordinator
OPDA Travel Coordinator
Bus Operators
(Whippet & Stagecoach)
Locke Hotel
Car Club operator (Enterprise)
Outspoken Cycles
Resident representatives
Swirles Court (Girton College)
Hill & Other Developers
Mears (operational maintenance)
Nursery
Travel Coordinator
Retailers
Bike Works CIC
Transport Stakeholders Group

## Slide 13: Store opening times: Monday-Saturday 07:30 - 22:00hrs, Sunday 10:00 - 16:00hrs Total car parking spaces: (141) Disabled: 8 Parent toddler: 5 Standard Car Parking: 128 Cycle Parking spaces: 50 Nearest Public Transport: 200 metres – 90 buses during the survey period (07:00 - 19:00hrs Mon-Fri). Normal bus timetable: Monday - Friday 06:00 - 23:00hrs Saturday 07:00 - 23:00hrs and Sunday 07:00 - 20:00hrs
Sainsbury's Food Store -Eddington

## Slide 14
S106 Planning Condition compliance on trip generation
Support the annual Travel Plan monitoring
Exclude non-store trips from car park counts
Compare walking and cycling modes against the 2018 travel baseline
Utilise the data to inform phase two site master plan baseline.
Reasoning and requirements of TRICS Monitoring

## Slide 15: TRICS Comparison store data:
The Transport Assessment reported the following Total 12 hour Base Case Person Trip generation mode shares for the Food Store:
TA prediction (2010)
TRICS survey (TRICS – May 2023)

## Slide 16
GFA range of 1,200m2 to 9,200m2.
All surveys from 01/01/2000 onwards.
Weekday only surveys (Monday-Friday (noting that most surveys were on Fridays)).
Location type to include: Edge of Town, Suburban Area, Neighbourhood Centre.
Sub-location types excluded: Retail Zone, Commercial Zone, Built-Up Zone, High Street.
All sites with a PFS included in the survey were excluded.
Highest population range within 1 mile is excluded (50,001-100,000).
Highest population range within 5 miles is excluded (500,001 or more).
TRICS Comparison store data:
SITE - REF | DESCRIPTION | TOWN/CITY | AREA | GFA | DAY | DATE
AR-01-A-01 | TESCO | DUNGANNON | ARMAGH | 2416 | FRI | 15/11/2002
CA-01-04 (EDDINGTON) | SAINSBURY'S | CAMBRIDGE | CAMBRIDGESHIRE | 3145 | WED | 17/05/2023
CP-01-A-01 | SAINSBURY'S | PONTLLANFRAITH | CAERPHILLY | 7124 | FRI | 07/10/2011
DC-01-A-13 | CO-OP PIONEER | BRIDPORT | DORSET | 1487 | FRI | 07/07/2000
DE-01-A-01 | SAINSBURY'S | LONDONDERRY | DERRY | 4042 | FRI | 15/11/2002
DV-01-A-21 | MORRISONS | PLYMOUTH | DEVON | 5000 | FRI | 23/10/2009
IA-01-A-01 | CO-OP | MENAI BRIDGE | ISLE OF ANGLESEY | 1825 | MON | 13/07/2009
LE-01-A-02 | ASDA | LEICESTER | LEICESTERSHIRE | 8900 | TUE | 23/06/2009
NM-01-A-03 | SAINSBURY'S | NORTHAMPTON | WEST NORTHAMPTONSHIRE | 7012 | FRI | 07/10/2011
SC-01-A-12 | SAINSBURY'S | WOKING | SURREY | 8250 | FRI | 23/11/2012
TW-01-A-02 | ASDA | NEWCASTLE UPON TYNE | TYNE & WEAR | 9050 | FRI | 03/05/2019
WN-01-A-10 | SAINSBURY'S | SLOUGH | WINDSOR & MAIDENHEAD | 6065 | FRI | 07/10/2011
WO-01-A-02 | WAITROSE | WORCESTER | WORCESTERSHIRE | 4780 | FRI | 27/09/2019
WS-01-A-10 | TESCO | CHICHESTER | WEST SUSSEX | 6003 | FRI | 21/07/2000

## Slide 17: TRICS: Rank order for land use 01 - RETAIL/A - FOOD SUPERSTORE (Pedestrian Trip Rates per 100m2 GFA (Arrivals + Departures)) Time Range: 07:00-22:00
Chart: 
| Pedestrians
Eddington Sainsbury | 113.32
WS-01-A-10 | 17.275
DC-01-A-13 | 41.42
IA-01-A-01 | 30.904
LE-01-A-02 | 18.012
WN-01-A-01 | 11.096
NM-01-A-03 | 7.772
DE-01-A-01 | 32.187
DV-01-A-21 | 35.62
WO-01-A-02 | 24.121
AR-01-A-01 | 32.533
SC-01-A-12 | 35.346

## Slide 18: TRICS: Rank order for land use 01 - RETAIL/A - FOOD SUPERSTORE (Bus/Tram and Cyclist Trip Rates per 100m2 GFA (Arrivals + Departures) Time Range: 07:00-22:00
Chart: 
| Bus/Tram | Cyclist
Eddington Sainsbury | 24.229 | 11.606
WS-01-A-10 | 11.495 | 5.897
DC-01-A-13 | 0.336 | 3.363
IA-01-A-01 | 0.493 | 1.534
LE-01-A-02 | 1.944 | 1.326
WN-01-A-01 | 0.923 | 1.154
NM-01-A-03 | 1.098 | 0.828
DE-01-A-01 | 3.661 | 0.668
DV-01-A-21 | 3.98 | 0.6
WO-01-A-02 | 1.172 | 0.586
AR-01-A-01 | 8.982 | 0.373
SC-01-A-12 | 1.976 | 0.266

## Slide 19: TRICS: Rank order for land use 01 - RETAIL/A - FOOD SUPERSTORE (Total Vehicles and Vehicle Occupants Trip Rates per 100m2 GFA (Arrivals + Departures)) Time Range: 07:00-22:00
Chart: 
| Total Vehicles | Vehicle Occupants
Eddington Sainsbury | 63.339 | 80.795
WS-01-A-10 | 185.74 | 291.787
DC-01-A-13 | 189.173 | 275.185
IA-01-A-01 | 154.082 | 219.945
LE-01-A-02 | 105.585 | 156.876
WN-01-A-01 | 150.206 | 191.377
NM-01-A-03 | 137.236 | 176.611
DE-01-A-01 | 201.262 | 316.923
DV-01-A-21 | 211 | 306.56
WO-01-A-02 | 99.582 | 151.401
AR-01-A-01 | 196.482 | 297.476
SC-01-A-12 | 79.091 | 108.885

## Slide 20: Eddington Full Modal Split
Full Modal split Excluding Eddington
Full Modal split Including Eddington
Comparison Sites Full Modal Split

## Slide 21
Eddington is demonstrating its phase one vision of being a sustainable development by:
Designing and building a community, where car ownership is not a requirement to live.
Delivery of social infrastructure within phase one of the development, i.e. Primary school, Nursery, Hairdressers, Bars, Restaurants, Hotel, Retail
Limited number of public on-street parking spaces and resident parking to discourage car ownership
The provision of walking and cycling routes to key onward destinations was key to the initial phase one
Where the public transport provision was achieved early and supports access to within 400Mtrs of most University sites/buildings
Continued support for on-site access to public hire E-mobility e-bikes /Scooters through Voi.
Reflections:

## Slide 22
West Hub Monitoring - in progress
West Cambridge Innovation Development
Creation of Cambridge-centric Data. (Labs, Hubs, Etc) to support trip banking reporting.
Trip data-driven support for the “reshaping the estate” program, with independently validated trip data.
University of Cambridge

## Slide 23: Thank you for your interest. Eddington-cambridge.co.uk
Greg Callaghan
greg.callaghan@stantec.com
Stewart Bethell
stewart.bethell@admin.cam.ac.uk